## Slide 1
PROJECT SUMMARY — KEY RESULTS
PROJECT RESULT
MAIN 1 OF 4
The project verifies the Tessent/circuit flow, signal behavior, and reusable automation with traceable evidence.
KEY RESULTS
THREE VERIFIED RESULTS
✓ | Result | Verified scope | Evidence
✓ | Flow & circuit | • Inserted RTL, ICL, PDL, SDC, and import.tcl • Correct PDL vectors and simulation patterns • Preserved netlist.vg, clean timing reports, and RTL/GLS consistency | • Insertion / ICL reports • Pattern and waveform evidence • Synthesis / timing / GLS reports
✓ | Config input | Basic and team-scale configs prepared | CSV / Tcl config
✓ | IJTAG insertion | Host IJTAG, SIB, and TDR inserted | Insertion log / RTL
✓ | Signal behavior | • Single-die HostIJTAG path and PDL I/O • Single-die PTAP-to-HostSTAP control signals • Stack-level selected-die path and retargeted PDL I/O | • Local waveform • STAP waveform • Retargeted PDL and stack waveform
✓ | ICL / PDL generation | Models and procedures generated | ICL / PDL files
✓ | Pattern retargeting | Target-specific patterns generated | Retarget report
✓ | Automation | • Basic-die and team-scale-die execution • Configuration response and repeatability • Consolidated reports and handoff artifacts | • Run log and config diff • Output / report comparison • HTML report and artifact inventory
✓ | Synthesis / GLS | Inserted access path preserved | Netlist / GLS log
✓ | Automation report | Execution summary and inventory generated | HTML / report diff
Project value is summarized on the left; the three result categories are verified on the right.
1
PROJECT PURPOSE
Build one reusable frontend flow that connects IEEE 1687 instrument access through an IEEE 1838 die hierarchy—from Tessent insertion to synthesis, GLS, and automated reporting.
KEY RESULTS
FLOW & CIRCUIT VERIFIED — complete Tessent outputs, PDL patterns, synthesized netlist, timing reports, and RTL/GLS behavior were verified.
SIGNAL BEHAVIOR VERIFIED — two parallel single-die tests and one stack-level test confirmed the intended paths and control behavior.
AUTOMATION VERIFIED — the configuration-driven procedure supports design changes, repeatable runs, consolidated reports, and project handoff.
ENGINEERING VALUE
Less repeated setup, faster migration across design hierarchies, and evidence that is easier to review and hand off.
REUSABLE FLOW • FASTER MIGRATION • TRACEABLE EVIDENCE

## Slide 2
RESULT 1 — TESSENT FLOW & CIRCUIT INTEGRITY
FLOW / STRUCTURE
MAIN 2 OF 4
The Tessent access flow and inserted circuitry were verified from DFT insertion and synthesis handoff through gate-level simulation.
VERIFICATION RESULT
PASS — Complete evidence chain confirmed
Tessent deliverables, PDL/pattern execution, netlist/timing integrity, and RTL-to-gate consistency were verified.
The generated reports provide traceable evidence from insertion and synthesis handoff through GLS.
2
Check item | What was verified | Acceptance criterion | Primary evidence | Status
Tessent deliverables | PTAP/STAP/IJTAG circuitry plus ICL, PDL, SDC, and import.tcl are generated | The intended hierarchy and all downstream synthesis handoff files are complete | • Insertion / ICL reports • Artifact inventory | PASS
PDL & pattern | Tessent-generated PDL vectors and simulation patterns execute correctly | Expected access operations and pattern compare checks pass | • PDL / vector files • Pattern report • RTL waveform | PASS
Netlist & timing | netlist.vg completely preserves the inserted test-access circuitry | Hierarchy and access paths remain intact PPA analysis reports show no errors and output normally | • netlist.vg • Synthesis report • Timing analysis reports | PASS
RTL-to-gate consistency | The same access sequence runs on the synthesized gate netlist | RTL/GLS behavior and care bits match | • GLS waveform • Compare log | PASS

## Slide 3
RESULT 2 — SIGNAL VERIFICATION
FUNCTIONAL RESULT
MAIN 3 OF 4
Each scenario verifies both the intended access path and the corresponding TDI/TDO or PTAP-controlled signal behavior.
RESULT: HostIJTAG and stack-level TDI/TDO behavior matched their PDL patterns, while HostSTAP produced the expected PTAP-controlled signals.
Two parallel single-die tests plus one end-to-end stack-level test.
3
Scenario | Access route | What the waveform proves | Evidence | Result
Single-Die HostIJTAG | PTAP → HostIJTAG → SIB/TDR | The correct path reaches target TDR TDI stimulus and TDO response follow the expected PDL pattern | • Generated PDL • Local waveform | PASS
Single-Die HostSTAP | PTAP → HostSTAP | The correct STAP path is selected PTAP control produces the expected STAP signals | • STAP waveform | PASS
Stack-Level Access | stack_top → selected die → target TDR | The correct stack path reaches the selected die data TDI stimulus and TDO response follow the retargeted PDL pattern | • Retargeted PDL • Stack waveform | PASS

## Slide 4
RESULT 3: AUTOMATION FLOW
FLOW VERIFICATION
MAIN 4 OF 4
One configuration-driven procedure completed both basic-die and team-scale-die flows, responded to configuration changes, and generated traceable handoff artifacts.
HANDOFF PACKAGE
✓ Configs ✓ Tcl procedures ✓ Inserted RTL / TSDB ✓ ICL / PDL ✓ Retargeted patterns ✓ RTL / GLS logs ✓ HTML report
Automation is verified through cross-design portability, configuration response, repeatability, consolidated reporting, and a complete handoff package.
4
Automation check | Verified outcome | Evidence | Status
Clean end-to-end run | All enabled stages complete from one entry point | • Top run log | PASS
Example die | The reference configuration completes the full flow | • Generated outputs • Flow report | PASS
Team complex die | The same core procedure supports the larger hierarchy | • Configuration • Inserted RTL | PASS
Configuration change | Generated hierarchy and outputs follow the revised configuration | • Config diff • Output diff | PASS
Repeatability | Repeated input reproduces the same structure and summary | • Report comparison | PASS
Report generation | Logs, artifacts, and results are consolidated for review and handoff | • HTML report • Artifact inventory | PASS