## Slide 1
PROGRESS REVIEW
IEEE 1687 / 1838
Automated Insertion & Verification
A repeatable flow linking Tessent RTL insertion, ICL/PDL retargeting, synthesis, and gate-level verification.
6
STAGES
3 validation levels
1
ENV
2
INSERT
3
RETARGET
4
RTL VERIFY
5
SYNTHESIS
6
GATE VERIFY
Scope: 1687 only → 1687 + 1838 → stack_top | DWR excluded
IEEE 1687 / 1838 Automation Progress Review
01

## Slide 2
CORE MESSAGE
One Reusable Engineering Flow, Not Three Isolated Cases
The same insertion, retargeting, simulation, and synthesis methods scale across deeper access hierarchies.
LEVEL 1
IEEE 1687
Local instrument access
LEVEL 2
1687 + IEEE 1838
Die-level access
LEVEL 3
stack_top
Multi-die hierarchical access
KEY TAKEAWAY
The flow is repeatable, extensible, and backed by clear acceptance evidence at every stage.
Architecture based on the current prototype and IEEE 1687-2014 / IEEE 1838-2019
02

## Slide 3
PRESENTATION LOGIC
Task and Checkpoint Can Share a Slide—Evidence Must Close the Loop
1
TASK
Action Taken
Example: insert SIB/TDR, generate ICL, and run retargeting
2
CHECKPOINT
Acceptance Criteria
Example: DRC passes, path is reachable, and care-bit mismatches = 0
3
EVIDENCE
Proof to Show
log summary
hierarchy
waveform / compare report
Definition of Done
Task completed + Checkpoint met + Evidence reproducible
Every stage uses this structure, so acceptance criteria never have to be hunted across slides.
Current scope: IEEE 1687 + IEEE 1838; DWR excluded
03

## Slide 4
MASTER FLOW
Six Stages Form a Repeatable End-to-End Automation Flow
01
Environment
script / file list
02
RTL Insertion
1687 / 1838 structures
03
ICL / PDL
retargeted patterns
04
RTL Verify
causal waveform trace
05
Synthesis
dont_touch + SDC
06
Gate Verify
same-pattern compare
One Flow, Three Levels
IEEE 1687
✓
Local instrument access
1687 + IEEE 1838
✓
Die wrapper + local IJTAG
stack_top
✓
Package-to-die hierarchical access
Current scope: IEEE 1687 + IEEE 1838; DWR excluded
04

## Slide 5
VALIDATION STRATEGY
Validation Depth Increases While the Core Flow Stays the Same
LEVEL 1
IEEE 1687
TAP → SIB → TDR → Instrument
LEVEL 2
1687 + IEEE 1838
PTAP / 3DCR / STAP + local IJTAG
LEVEL 3
stack_top
Multiple STAPs + hierarchical retargeting
+ wrapper control
+ multi-die access depth
Shared core: one Tcl / ICL / PDL / simulation / synthesis flow
Current scope: IEEE 1687 + IEEE 1838; DWR excluded
05

## Slide 6
STAGE DETAIL
Convert One-Off Commands into a Repeatable Environment
1 ENV
2 INSERT
3 RETARGET
4 RTL VERIFY
5 SYNTHESIS
6 GATE VERIFY
Current scope: IEEE 1687 + IEEE 1838; DWR excluded
06
STAGE 1
Environment & Script Setup
TASK
Actions
CHECKPOINT
Pass Conditions
EVIDENCE
Artifacts
Organize RTL, libraries, and file lists
Create one entry point for insertion, pattern generation, simulation, and synthesis
Switch among 1687, 1838, and stack_top through configuration
✓
All RTL reads and elaborates successfully
✓
A clean directory reproduces the full run
✓
Changing configurations requires no major manual script edits
Clean-run log
Fixed entry point and output structure
Config diff
Only parameters change across the three architectures
Generated artifacts
RTL / ICL / pattern / reports

## Slide 7
STAGE DETAIL
Automated Insertion Must First Prove Reachability and RTL Integrity
1 ENV
2 INSERT
3 RETARGET
4 RTL VERIFY
5 SYNTHESIS
6 GATE VERIFY
Current scope: IEEE 1687 + IEEE 1838; DWR excluded
07
STAGE 2
Automated RTL Insertion
Functional RTL
original design
+ instrument ports
Tessent-inserted RTL
TAP / PTAP
SIB
TDR
3DCR
STAP
Checkpoint
✓
Insertion DRC passes
✓
Every instrument is reachable through the network
✓
Generated hierarchy and connectivity match the intended architecture
Evidence
successful insertion summary
generated hierarchy / instance count
compile / connectivity report
This stage proves correct insertion; the next stage proves correct operation.

## Slide 8
STAGE DETAIL
ICL/PDL Retargets Instrument Operations to Top-Level Patterns
1 ENV
2 INSERT
3 RETARGET
4 RTL VERIFY
5 SYNTHESIS
6 GATE VERIFY
Current scope: IEEE 1687 + IEEE 1838; DWR excluded
08
STAGE 3
ICL / PDL & Pattern Retargeting
Instrument PDL
write / run / read
Post-insertion ICL
SIB + die hierarchy
Retargeting
resolve access path
Top-level Pattern
package TDI/TDO sequence
Checkpoint
✓
ICL rule and syntax checks pass
✓
Retargeting completes with no unresolved paths
✓
Scan length matches the active network
Why it matters
Users describe only instrument-level operations; the tool handles SIBs, STAPs, and multi-die paths automatically.

## Slide 9
STAGE DETAIL
RTL Verification Traces the Full Causal Chain—not Just Simulation Completion
1 ENV
2 INSERT
3 RETARGET
4 RTL VERIFY
5 SYNTHESIS
6 GATE VERIFY
Current scope: IEEE 1687 + IEEE 1838; DWR excluded
09
STAGE 4
RTL Pattern Verification
TMS / TCK
drive state
TAP / PTAP
FSM transition
IR decode
select network
Capture / Shift / Update
enable registers
SIB / 3DCR / STAP
open path
TDR / shadow
write & read
PASS criteria
✓
All care-bit comparisons pass
✓
Instrument response matches expectations
✓
Unselected instruments remain unchanged
Evidence
Representative waveform with markers
pattern pass summary / mismatch = 0
reset、SIB / STAP close behavior

## Slide 10
RTL VERIFICATION EVIDENCE
One Pattern Flow Now Covers Three Access Depths
1 ENV
2 INSERT
3 RETARGET
4 RTL VERIFY
5 SYNTHESIS
6 GATE VERIFY
Current scope: IEEE 1687 + IEEE 1838; DWR excluded
10
01
IEEE 1687
TAP → SIB → TDR → Instrument
Proves local instrument access
✓
02
1687 + IEEE 1838
PTAP → local SIB → TDR
Proves wrapper, 3DCR, and STAP control
✓
03
stack_top
Package → Basic STAP → Sensor STAP → SIB → TDR
Proves multi-die retargeting and return path
✓
Access hierarchy grows; manual pattern complexity does not.

## Slide 11
RTL VERIFICATION EVIDENCE
Event Markers Make Complex Stack Traces Verifiable
1 ENV
2 INSERT
3 RETARGET
4 RTL VERIFY
5 SYNTHESIS
6 GATE VERIFY
Current scope: IEEE 1687 + IEEE 1838; DWR excluded
11
M0
Reset
M1
Basic 3DCR
M2
Sensor0 3DCR
M3
Sensor1 SIB
M4
TDR Update
M5
Start
M7
Valid
M8
Capture
M9
Compare
M10
Pass
Each marker binds the expected state, control, and data signals, localizing errors to IEEE 1838 access, IEEE 1687 selection, or instrument behavior.

## Slide 12
STAGE DETAIL
Synthesis Must Preserve the Test Network—not Merely Produce a Netlist
1 ENV
2 INSERT
3 RETARGET
4 RTL VERIFY
5 SYNTHESIS
6 GATE VERIFY
Current scope: IEEE 1687 + IEEE 1838; DWR excluded
12
STAGE 5
Synthesis Integration
Tessent RTL
generated test logic
Compile test block
independent boundary
dont_touch + SDC
preserve structure / timing
Top synthesis
functional + test logic
Gate netlist
ready for GLS
Checkpoint
✓
Tessent network survives optimization intact
✓
Test clocks, resets, and generated constraints are applied correctly
Evidence
pre/post-synthesis hierarchy & instance comparison
synthesis log / constraint report / gate netlist

## Slide 13
STAGE DETAIL
Gate-Level Reuse Proves Synthesis Preserved the Access Path
1 ENV
2 INSERT
3 RETARGET
4 RTL VERIFY
5 SYNTHESIS
6 GATE VERIFY
Current scope: IEEE 1687 + IEEE 1838; DWR excluded
13
STAGE 6
Gate-Level Verification
RTL lane
Gate lane
Inserted RTL
Same retargeted pattern
Expected response
Gate netlist + libs
Same retargeted pattern
Observed response
COMPARE
care bits
mismatch = 0
Gate netlist compiles • pattern completes • RTL/gate readback matches • no unexpected X affects comparison

## Slide 14
COVERAGE SUMMARY
Regression Matrix Shows Completed Coverage at a Glance
Each column represents an access depth; each row is an accepted end-to-end deliverable.
DWR excluded
Verification item | 1687 | 1687 + 1838 | stack_top
Automated RTL insertion | ✓ | ✓ | ✓
ICL generation / check | ✓ | ✓ | ✓
PDL retargeting | ✓ | ✓ | ✓
RTL pattern simulation | ✓ | ✓ | ✓
Synthesis integration | ✓ | ✓ | ✓
Gate-level pattern simulation | ✓ | ✓ | ✓
Hierarchical access | N/A | Local die | Multi-die
Conclusion: the complete flow now spans local to multi-die access, with closed-loop verification at both RTL and gate levels.
Current scope: IEEE 1687 + IEEE 1838; DWR excluded
14

## Slide 15
WHAT WAS BUILT
The Engineering Value Is Repeatability, Scalability, and Traceability
01
REPEATABLE
Rerun insertion, retargeting, simulation, and synthesis from a clean environment
02
SCALABLE
Scale the same flow from 1687 to 1838 and then to a multi-die stack
03
TRACEABLE
Attach a checkpoint plus a log, waveform, or compare result to every stage
Integration Issues Resolved
Test logic
independent compile + dont_touch + Tessent SDC
Retargeting
instrument-level PDL → package-level pattern
The result is not a one-time PASS, but a reusable baseline for future designs.
Current scope: IEEE 1687 + IEEE 1838; DWR excluded
15

## Slide 16
CURRENT STATUS
End-to-End Baseline Complete; Regression Hardening Is Next
✓
ENV
✓
INSERT
✓
RETARGET
✓
RTL VERIFY
✓
SYNTHESIS
✓
GATE VERIFY
COMPLETED
✓
1687 / 1838 automated insertion
✓
ICL / PDL retargeting + RTL verification
✓
synthesis integration + gate-level verification
NEXT
Curate representative logs, waveforms, and compare reports
Build one-command regression with assertion-based checks
Confirm project integration order; evaluate DWR in a later phase
Core message: the flow works end to end; next, improve automation maturity and evidence reproducibility.
Decision point: regression hardening first; DWR remains out of current scope
16