## Slide 1
DFT INTEGRATION PROJECT
A Reusable RTL-to-Stack
DFT Integration Flow
IEEE 1687 · IEEE 1838 · Stack Retargeting · DWR Next Step
Tessent 2025.02 | Internal Technical Review
TARGET ARCHITECTURE
TOP DIE
LOCAL IJTAG
MIDDLE DIE
IJTAG + STAP
BASE DIE
PTAP · IJTAG + STAP
PTAP
SERIAL
ACCESS
DESIGN DATA
AUTOMATION
VERIFICATION
STANDARDIZED TEAM FLOW
DFT Integration Project · Internal Review
Notes: [Sources]
- https://www.siemens.com/en-us/products/ic/tessent/test/multi-die/
- https://resources.sw.siemens.com/en-US/fact-sheet-tessent-multi-die-software-for-3d-ic-designs/
[/Sources]

## Slide 2
A · PROBLEM
02
The gap is not Tessent capability—it is repeatable integration.
MANUAL DESIGN-BY-DESIGN EXECUTION
RTL A
RTL B
RTL C
insert_A.tcl
insert_B_v2.tcl
stack_fix.tcl
WARNING: no source
ERROR: inaccessible TDR
INFO: extraction completed
ERROR: retarget failed
WHAT THE TEAM STILL LACKS
Input contract: what a designer must provide
Role abstraction: Base / Middle / Top behavior
Quality gates: what counts as a valid result
Failure localization: where the flow must stop
Portable evidence: reports, ICL, patterns, simulation
TOOL RUN
≠
TEAM CAPABILITY
A tool run becomes a team capability only when inputs, decisions, and acceptance criteria are standardized.
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]

## Slide 3
B.1 · TESSENT IMPLEMENTATION
03
Tessent executes the RTL-to-stack flow through standardized handoffs.
TESSENT RTL EXECUTION · INSERT → EXTRACT → RETARGET → VERIFY
01
EXISTING
RTL
RTL · libraries
instrument ports
02
TESSENT
INSERTION
IEEE 1687 / 1838
post-DFT RTL
03
ICL / PDL
CONTEXT
network hierarchy
instrument intent
04
PACKAGE
RETARGET
stack_top · ICL
resolved path
05
VCS
VERIFICATION
waveform · compare
PASS / FAIL
TESSENT EXECUTION CONTRACT · INPUT, TOOL ACTION, AND EXIT EVIDENCE
CONTROL POINT
RTL LOAD
INSERT
EXTRACT
RETARGET
SIMULATE
KEY INPUT
golden RTL
filelist + libraries
resolved config
policy + die role
post-DFT RTL
instrument PDL
validated ICL
stack map
pattern
expected data
FLOW ACTION
read_design
resolve top + ports
process DFT spec
insert hardware
extract ICL
export TSDB
iApply / retarget
resolve package path
VCS run
compare care bits
EXIT EVIDENCE
elaborated design
resolved clock/reset
DFT DRC
post-DFT RTL
ICL + TSDB
declared targets
top-level pattern
no unresolved path
waveform + log
care mismatch = 0
Tessent is the execution engine; automation standardizes inputs, handoffs, and evidence.
DFT Integration Project · Internal Review
Notes: [Sources]
- https://www.siemens.com/en-us/products/ic/tessent/test/multi-die/
- https://resources.sw.siemens.com/en-US/fact-sheet-tessent-multi-die-software-for-3d-ic-designs/
[/Sources]

## Slide 4
B.1.1 · FILE CONTRACT
04
Each artifact has one defined purpose.
CORE FILE FAMILIES · INPUT → TOOL STATE → ICL + PDL → RETARGETED PROOF
ARTIFACT
OWNER / ORIGIN
WHAT IT CONTAINS
FLOW ROLE
TYPE
01 RTL / LIB
User design package
RTL + filelist
cell / library models
Read and elaborate the golden design.
INPUT
02 MANIFEST / TCL
User data → automation
die role + ports
resolved commands
Configure insertion without core-Tcl edits.
CONTROL
03 POST-DFT / TSDB
Tessent insertion
inserted RTL
saved design views
Hand off INSERT → EXTRACT / RETARGET.
WORKING DATA
04 ICL
IP or Tessent extraction
modules + ports
host / SIB / TDR links
Describe and resolve the access path.
ACCESS MODEL
05 PDL
IP / user procedure
iWrite / iRead / iApply
instrument operations
Retarget the procedure through ICL.
PORTABLE INTENT
06 PATTERN / LOG
Tessent + checker
top-level stimulus
expected / observed data
Run VCS and report PASS / FAIL.
EVIDENCE
DESIGN + CONTROL INPUTS
STANDARD ACCESS + GENERATED PROOF
ICL answers HOW TO REACH; PDL answers WHAT TO DO; retargeting combines both into a top-level pattern.
DFT Integration Project · Internal Review
Notes: Presenter cue: Separate the files by responsibility. ICL is the access-network model; PDL is the instrument procedure. Tessent retargeting combines both to create a top-level access pattern. TSDB is the Tessent working database used to preserve design views and stage handoffs, not a portable IEEE language.
[Sources]
- IEEE 1687-2014 overview: https://standards.ieee.org/ieee/1687/3931/
- Siemens Tessent IJTAG fact sheet: https://resources.sw.siemens.com/en-US/fact-sheet-tessent-ijtag/
- Siemens Tessent TSDB automation overview: https://blogs.sw.siemens.com/tessent/2020/03/06/the-quest-for-optimal-dft-automation/
- Internal project artifact names and current RTL-level flow supplied by the presenter.
[/Sources]

## Slide 5
B.2 · CIRCUIT ARCHITECTURE
05
Base, Middle, and Top roles map three access scopes onto one stack.
THREE ACCESS SCOPES · ROLE-AWARE STACK MODEL
TOP
LEVEL 1 · IEEE 1687
MIDDLE
LEVEL 2 · 1687 + 1838
BASE
LEVEL 3 · STACK ENTRY
SERIAL ACCESS
PTAP
COMMON PROCEDURE + ROLE-DEPENDENT CONFIGURATION
Configuration item
Base
Middle
Top
Serial-path role
Entry
Relay
Terminus
Local IJTAG
Required
Required
Required
Host definition
IJTAG + STAP
IJTAG + STAP
IJTAG
Downstream STAP
Yes
Yes
No
Stack interface
PTAP + upper
lower + upper
lower endpoint
Generated output
RTL + ICL
RTL + ICL
RTL + ICL
Core Tcl rewrite
No
No
No
ROLE = DATA
The same engine emits different host topology, ports, and artifacts from one role field.
Shared procedure plus role data supports every die position without rewriting core Tcl.
DFT Integration Project · Internal Review
Notes: [Sources]
- https://blogs.sw.siemens.com/eda-support/2024/06/01/introduction-to-tessent-multi-die/
[/Sources]

## Slide 6
B.3 · CURRENT PROGRESS
06
RTL access is verified across all three scopes
CURRENT RTL PROOF · IEEE 1687, IEEE 1687 + 1838, AND STACK_TOP
ACCESS
IMPLEMENTED PATH
DELIVERABLES
ACCEPTANCE
STATUS
01 IEEE 1687
TAP → SIB → TDR → instrument
inserted RTL
ICL + PDL
Local access and instrument response confirmed.
DONE
02 1687 + 1838
PTAP → 3DCR / STAP → local IJTAG
post-DFT RTL
ICL + TSDB
Wrapper control and local TDR reachability confirmed.
DONE
03 STACK_TOP
Package → STAP chain → SIB / TDR
stack_top
stack ICL
Multi-die access path and return confirmed.
DONE
04 RETARGET
Instrument PDL → package / stack path
pattern
reachable-target list
No unresolved path; declared targets are reachable.
DONE
05 RTL SIM
Generated pattern → VCS checker
waveform
compare log
Care-bit mismatch = 0; expected TDR value observed.
DONE
06 AUTOMATION
CSV → Python / Tcl → Tessent / VCS
generated handoffs
run evidence
One design input reproduces the complete RTL access run.
DONE
CURRENT RTL BASELINE
DWR / COMPLEX DIE = NEXT STEPS
All current claims are supported by RTL, ICL/PDL, retargeting, and VCS evidence.
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]

## Slide 7
C.1 · CLEAN PIPELINE
07
Every run starts from golden RTL and promotes only validated artifacts.
CLEAN AND REPRODUCIBLE EXECUTION
00
CLEAN
Create an isolated run directory
01
PRECHECK
Parse manifest; reject missing inputs
02
CONFIG
Generate role-specific Tessent data
03
INSERT
Insert IEEE 1687 / 1838 hardware
04
EXTRACT
Export post-DFT RTL, ICL, and TSDB
05
PROVE
Retarget, simulate, and archive evidence
PHASE EXIT CONTRACT · WRITE ONLY AFTER THE GATE PASSES
STAGE
PRIMARY WRITE
BLOCK / STOP CONDITION
CLEAN
run directory
dirty or reused inserted RTL
PRECHECK
input audit
missing file, top, clock, reset
CONFIG
resolved config
unknown role or unresolved port
INSERT
post-DFT RTL
DFT DRC or hierarchy failure
EXTRACT
ICL + TSDB
no-source / no-destination path
PROVE
pattern + sim log
unreachable TDR or care mismatch
FAIL FAST
No downstream artifact is promoted after a failed gate.
The flow is deterministic: same inputs, same stages, same evidence package.
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]

## Slide 8
C.2 · GRADUATE DESIGN QUALITY
08
Quality gates distinguish “tool completed” from “access proven.”
PROGRESSIVE VERIFICATION · GATE, EVIDENCE, ACCEPTANCE RULE, AND FAILURE ACTION
GATE
QUESTION
PRIMARY EVIDENCE
PASS CONDITION
FAILURE ACTION
01 REPORT
Was the intended hierarchy created?
report_config_data
resolved configuration
Expected hosts, SIBs, TDRs, and ports are present.
Stop configuration; fix manifest or role mapping.
02 VALIDATE
Are configuration and connections legal?
DFT DRC
validate-only log
No illegal host, unconnected source, or unresolved destination.
Stop insertion; localize the first structural error.
03 EXTRACT
Does ICL represent inserted RTL?
extracted ICL
TSDB hierarchy
ICL paths and ports match the post-DFT hardware hierarchy.
Reject artifact; do not promote to stack build.
04 RETARGET
Can PTAP reach every declared instrument?
retargeted pattern
reachable-target list
Reachable / declared instruments = 100%.
Trace host root, SIB state, and stack connection.
05 SIMULATE
Does the generated pattern behave correctly?
waveform + compare log
care-bit counter
Care-bit mismatch = 0 and expected TDR value is observed.
Trace CE / SE / UE, TDI/TDO, and update timing.
06 RERUN
Can identical inputs reproduce the same result?
rerun summary
archived evidence
Same manifest reproduces reachable targets and 0 care-bit mismatch.
Diff inputs and stage artifacts; stop promotion.
GENERATION SUCCESS
ACCESS + REPRODUCIBILITY
A successful command is only an intermediate state; acceptance requires structural and behavioral evidence.
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]

## Slide 9
C.2.1 · TOPOLOGY REASONING
09
The HostIjtag + HostStap fix demonstrates topology-level design reasoning.
BEFORE · TWO INDEPENDENT ACCESS ROOTS
TAP
HostIjtag
HostStap
SIB → TDR
Upper die
×
TDR and SIB appear in the extracted ICL
Retarget cannot traverse to the intended target
Typical symptom: inaccessible / no-source path
AFTER · ONE INTENDED HOST TOPOLOGY
TAP
Unified host configuration
Local IJTAG
SIB → TDR
Downstream STAP
Upper-die access
RETARGETABLE PATH
HostIjtag + HostStap are created in the same configuration transaction.
DEBUG EVIDENCE · VISIBILITY ALONE IS INSUFFICIENT
CHECK
BEFORE
AFTER
ACCEPTANCE CRITERION
Access roots
2 independent roots
1 intended host root
One PTAP path owns local IJTAG and downstream STAP.
Extracted ICL
TDR / SIB visible
TDR / SIB visible
ICL topology matches the inserted RTL hierarchy.
Retarget
Upper target inaccessible
Upper target reachable
Reachable / declared targets = 100%.
Error signature
no-source / inaccessible
no unresolved path
No unresolved source, destination, or hierarchy mapping.
The fix came from topology reasoning—not from adding another Tessent command.
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]

## Slide 10
C.3 · ENABLE AUTOMATION
10
Design intent stays outside the reusable Tessent procedure.
USER-PROVIDED INPUTS
project/
├─ rtl/
├─ filelist.f
├─ libraries.tcl
├─ dft_manifest.yaml
└─ expected_results.yaml
Golden RTL and top module
Clock / reset and technology data
Die role and local instruments
Stack connectivity and expected results
AUTOMATION BOUNDARY
Python
ORCHESTRATION
Reusable Tcl
PROCEDURES
parse · validate · generate · dispatch
GENERATED DELIVERABLES
POST-DFT RTL
role-specific inserted design
ICL / TSDB
per-die and stack hierarchy
IMPORT / RETARGET
stack access procedures
PATTERNS
retargeted access tests
REPORTS / LOGS
review and rerun evidence
Rule: design-specific net names are referenced by the manifest, never embedded in core Tcl.
MANIFEST SCHEMA · THE USER EDITS VALUES; THE FLOW OWNS IMPLEMENTATION
PROJECT
top / files
clock / reset
ACCESS ROLE
base | middle | top
PTAP / STAP policy
LOCAL IJTAG
instrument / TDR list
SIB placement intent
STACK
die order
upstream / downstream
CHECKER
expected data
compare rules
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]

## Slide 11
C.3.1 · LOCAL-DIE AUTOMATION | RTL → RETARGET → VCS
ONE CSV
DRIVES THE COMPLETE
DFT-TO-PATTERN FLOW
Design intent is captured once; reusable Python/Tcl generates every local-die handoff through VCS pattern verification.
1 USER-MAINTAINED INPUT
REUSABLE PYTHON / TCL AUTOMATION CORE
DESIGN-SPECIFIC DATA STOPS AT THE CSV
USER PROVIDES
design_config_
<die>.csv
DIE-SPECIFIC SOURCE
[DESIGN]
name · top · RTL list
base / middle / top role
[TDR]
instrument · data ports · PDL
[STAP]
secondary TAP ports
stack-access definition
[RETARGET]
clock · reset · black boxes
pattern environment
01
CONFIGURE
gen_read_config.py
Builds the die-specific Tessent setup from the CSV.
OUTPUTS
insert_vars.tcl — setup
ijtag_spec.tcl — host map
02
INSERT DFT
run_insert.sh
Runs Tessent insertion and exports the local-die database.
OUTPUTS
dft_inserted.v — inserted RTL
design.icl / dft.tsdb — access DB
03
DISCOVER ICL
parse_icl.py
Finds instruments and builds the retarget context.
OUTPUTS
retarget_vars.tcl — setup
retarget_info.txt — paths
04
RETARGET
run_retarget.tcl
Generates access and STAP-routing patterns.
OUTPUTS
local_patterns.v — VCS pattern
STAP / PDL — route + operations
05
VERIFY
run_sim.sh
Runs VCS and checks the serial-access waveform.
OUTPUTS
sim.log / waveform DB
PASS / FAIL — data check
✓
LOCAL-DIE RESULT
VCS PATTERN
VERIFICATION
retargeted pattern executes
waveform checked · verdict recorded
AUTOMATION CONTRIBUTION
DESIGN DATA ENTERS ONCE — EVERY FILE HANDOFF IS GENERATED, EXPLAINED, RETARGETED AND VERIFIED.
BLUE = REUSABLE | ORANGE = GENERATED | GREEN = INPUT / VERIFICATION
11
Notes: [Sources]
- User-provided local-die DFT workflow and filenames; no external assets or claims used.

## Slide 12
D · CONCLUSION
12
The deliverable is reusable infrastructure—not isolated commands.
WHAT THIS PROJECT ADDS TO THE TEAM
01
REUSABLE
INTEGRATION
Separates design-specific inputs from the reusable Tessent procedure.
02
PROGRESSIVE
CORRECTNESS
Defines gates from configuration reports to stack-level simulation evidence.
03
SCALABLE
DEPLOYMENT
Supports different die roles, instruments, and stack structures; DWR remains the next extension.
CAPABILITY OWNERSHIP AND PROJECT STATUS
TEAM NEED
TESSENT PROVIDES
THIS PROJECT PROVIDES
STATUS
Per-die IEEE 1687 / 1838
Insertion / extraction commands
Role abstraction + reusable configuration
DONE
Stack access
ICL import and retarget engine
Unified topology + generated stack/import flow
DONE
DWR link verification
Wrapper and pattern capability
Plan: port inventory + mapping + link result matrix
NEXT
Design portability
Execution on a supplied design
Input contract + gates + regression evidence
NEXT
Completed: per-die 1687/1838 + stack retarget/VCS. Next: complex die + DWR. ATPG excluded.
The deliverable is a flow the team can adopt, review, hand off, and extend.
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]

## Slide 13
NEXT STEPS
13
Next steps: complex die insertion, DWR proof, then GUI/report.
DFT Integration Project · Internal Review
AUTOMATED BASELINE
ONE CONFIGURATION → GENERATED RTL / ICL / STACK / PATTERN / CHECK
01
INPUT CONTRACT
manifest fields
Python pre-check
✓
02
DFT CONFIG
config Tcl
validated host setup
✓
03
PER-DIE INSERT
post-DFT RTL
per-die TSDB
✓
04
ICL EXTRACT
die.icl
resolved access paths
✓
05
STACK COMPOSE
stack_top / stack.icl
import Tcl
✓
06
RETARGET + VCS
pattern + expected data
VCS checker
✓
NEXT · NOT YET IMPLEMENTED
USE THE TEAM'S COMPLEX RTL AS A NEW DIE; PROVE DWR ACCESS INSIDE THE STACK
07
COMPLEX DIE
Onboard the supplied RTL
as a reusable die input
08
DWR INSERT
Build wrapper inventory
and external-mode chain
09
STACK INTEGRATE
Compose the new die
and retarget access
10
DWR PROOF
Execute link pattern
and pass comparison
11
GUI / VISUAL REPORT
Launch the automated run · track accountable stage status · export PASS/FAIL, link matrix, runtime, and evidence package
SCOPE · IEEE 1687 / 1838 + DWR · ATPG / EDT / FAULT COVERAGE EXCLUDED
Notes: [Sources]
- Internal project scope and progress supplied by the presenter.
[/Sources]

## Slide 14
BACKUP · DWR IMPLEMENTATION PLAN
14
Planned DWR wrappers control and observe die-to-die links.
LINK-LEVEL HARDWARE VIEW
SOURCE DIE
functional logic
DWR
CAPTURE / DRIVE
DWR
CAPTURE / DRIVE
DESTINATION DIE
functional logic
→
→
↓
DIE-TO-DIE INTERCONNECT
control / observe at the die boundary
TARGET DWR PORT INVENTORY (TBD)
LINK
D
SOURCE
DEST.
W
CLOCK / MODE
DATA
UP
TBD
TBD
16
TBD / extest
CFG
DN
TBD
TBD
8
TBD / extest
IRQ
DN
TBD
TBD
1
async / observe
Structural: port, direction, width, and die ownership
Configuration: source-drive / destination-capture mapping
Behavioral: pattern, expected value, waveform, and compare
Coverage: one sign-off row per declared functional link
INVENTORY
CHECK
DWR
CONFIG
LINK
PATTERN
PASS / FAIL
MATRIX
COVERAGE
verified / declared
Target contract only; port mapping, patterns, and results follow DWR insertion.
DFT Integration Project · Internal Review
Notes: [Sources]
- https://grouper.ieee.org/groups/3Dtest/statusReports/P1838-StatusReport-161115-itc16slides.pdf
[/Sources]

## Slide 15
BACKUP · COMPLEX-DIE PROOF PLAN
15
The team's complex RTL die will prove portability without core-Tcl rewrites.
CURRENT BASELINE
NEXT TARGET · NOT IMPLEMENTED
SENSOR DIE 2
local instrument
SENSOR DIE 1
local instrument
ALU BASE DIE
PTAP · local instrument
TEAM COMPLEX RTL
functional ports
DWR-ENABLED DIE
capture / drive
STACK BASE
PTAP · stack access
D2D
LINKS
PORTABILITY ACCEPTANCE MATRIX · VALUES BELOW ARE DEMONSTRATION TARGETS, NOT COMPLETED RESULTS
PROPERTY
BASELINE STACK
COMPLEX TARGET
DESIGN DATA EDIT
CORE PROCEDURE
Die roles
Base + 2 sensor endpoints
existing stack + new die
dft_manifest.yaml
unchanged
Local access
3 local instruments
local IJTAG + new-die ports
instrument list
unchanged
Functional links
none required
actual team link inventory
dwr_ports.csv
unchanged
Required proof
PTAP → every local TDR
PTAP access + every DWR link
expected-results file
unchanged
Sign-off KPI
100% reachable; 0 mismatch
100% reachable; all links pass
generated reports
0 Tcl rewrites
Success means the second design requires new design data, not a rewritten Tessent flow.
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]

## Slide 16
BACKUP · MANIFEST CONTRACT
16
A manifest separates design intent from reusable DFT implementation.
DESIGNER WORKSPACE
project/
├─ rtl/
│ ├─ base_top.sv
│ └─ blocks/*.sv
├─ filelist.f
├─ libraries.tcl
├─ dft_manifest.yaml
├─ instruments.yaml
├─ stack_connections.csv
├─ dwr_ports.csv
└─ expected_results.yaml
EXAMPLE MANIFEST
project: sensor_stack
top: middle_die_top
die_role: middle
clock:
port: tck
edge: rising
reset:
port: trst_n
active: low
ijtag:
host: main
instruments: instruments.yaml
stack:
downstream: top_die
dwr:
inventory: dwr_ports.csv
FIELD OWNERSHIP AND VALIDATION
FIELD
CONSUMER
REJECT WHEN
top / filelist
RTL reader
unresolved
die_role
role resolver
illegal role
clock / reset
DFT config
missing port
ijtag.host
host builder
role conflict
instruments
TDR / SIB
bad width
stack link
stack composer
unmapped
dwr.inventory
planned DWR stage
not enabled / dir-width
expected data
sim checker
missing value
DESIGN DATA
→
VALIDATED SCHEMA
→
GENERATED TOOL PLAN
Core Tcl never changes for a new legal value set.
The integration boundary is explicit: designers own intent; automation owns translation and validation.
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]

## Slide 17
BACKUP · MANIFEST VALIDATION
17
Field ownership makes manifest errors fail fast.
FIELD OWNERSHIP AND VALIDATION
FIELD
CONSUMER
REJECT WHEN
top / filelist
RTL reader
module or file unresolved
die_role
role resolver
not base / middle / top
clock / reset
DFT config
port missing or polarity unknown
ijtag.host
host builder
conflicts with role policy
instruments
TDR / SIB builder
instance or width invalid
stack link
stack composer
die or port mapping missing
dwr.inventory
planned DWR stage
reserved for next step
expected data
simulation checker
target or compare value absent
Core Tcl never changes for a new legal value set.
The integration boundary is explicit: designers own intent; automation owns translation and validation.
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]

## Slide 18
BACKUP · EVIDENCE PACKAGE
18
Each run produces a complete, reviewable evidence package.
RUN-SCOPED ARTIFACT TREE
run_2026xxxx_xxxx/
├─ 00_inputs/
│ ├─ resolved_manifest.yaml
│ └─ input_audit.json
├─ 01_config/
│ ├─ generated_config.tcl
│ └─ report_config_data.log
├─ 02_per_die/
│ ├─ post_dft_rtl/
│ ├─ die.icl
│ └─ tsdb/
├─ 03_stack/
│ ├─ stack_top.*
│ ├─ stack.icl
│ └─ import.tcl
├─ 04_patterns/
└─ 05_simulation/
EVIDENCE MATRIX
ARTIFACT
CREATED BY
WHAT IT PROVES
PRIMARY CONSUMER
manifest
Python pre-check
exact inputs and resolved defaults
flow owner / regression
config report
Tessent configuration
host, SIB, TDR, and role intent
DFT reviewer
post-DFT RTL
per-die insertion
implemented test hardware
RTL / integration
per-die ICL + TSDB
extract phase
hardware access description
stack composer
stack_top + stack ICL
stack phase
die order and serial connectivity
retarget engine
import / retarget Tcl
stack generator
reproducible target selection
pattern generation
pattern + expected data
retarget
intended control and observation
simulation
simulation report
checker
behavioral pass / fail evidence
sign-off / handoff
A run is promotable only when the artifact set is complete and internally consistent.
The evidence package makes results reproducible, debuggable, reviewable, and transferable to another engineer.
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]

## Slide 19
BACKUP · FAILURE OWNERSHIP
19
Each failure maps to one owning stage and next action.
DETERMINISTIC STOP BOUNDARY
INPUT
CONFIG
INSERT
EXTRACT
RETARGET
SIMULATE
ARCHIVE
SYMPTOM-TO-OWNER MATRIX
OBSERVED SYMPTOM
OWNER
FIRST EVIDENCE TO OPEN
LIKELY ROOT
NEXT ACTION
Top module / port not found
INPUT
input_audit.json
filelist or manifest mismatch
correct input; restart from clean
Illegal host or role conflict
CONFIG
report_config_data.log
role policy or duplicate host root
fix role / host mapping
Insertion DRC failure
INSERT
insert log + post-DFT hierarchy
clock, reset, or unsupported connectivity
fix DFT config; reinsert
no source / no destination
EXTRACT
ICL port path + extraction log
floating or unmapped stack endpoint
repair RTL / stack connection
Instrument visible but inaccessible
RETARGET
reachable-target list + ICL route
wrong access root or closed SIB path
trace PTAP → host → SIB → TDR
Care-bit mismatch
SIMULATE
waveform + compare log
phase, edge, expected value, or TDO timing
trace CE / SE / UE and compare point
Evidence package incomplete
ARCHIVE
artifact-tree completeness check
missing pattern, log, or expected data
block handoff; regenerate missing artifact
The flow fails at the earliest accountable stage, so broken artifacts never contaminate downstream debug.
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]

## Slide 20
BACKUP · DWR SIGN-OFF PLAN
20
Planned DWR sign-off requires structural and behavioral evidence.
TARGET INTERFACE INVENTORY · TBD
LINK
SRC DIE.PORT
DST DIE.PORT
DIR
W
CLOCK
TEST INTENT
EXPECTED
DATA_UP
TBD
TBD
UP
TBD
TBD
drive / capture
TBD
CFG_DN
TBD
TBD
DN
TBD
TBD
drive / capture
TBD
IRQ_DN
TBD
TBD
DN
TBD
TBD
toggle / observe
TBD
PER-LINK VERIFICATION TRANSACTION
1 · INVENTORY
CHECK
2 · SOURCE
DRIVE
3 · INTERCONNECT
TRANSFER
4 · DESTINATION
CAPTURE
5 · COMPARE
+ ARCHIVE
SIGN-OFF RESULT MATRIX · TARGET FORMAT (VALUES TBD)
LINK
PORT / WIDTH
WRAPPER MAP
PATTERN
SIM COMPARE
RESULT
EVIDENCE
DATA_UP
TBD
TBD
TBD
TBD
OPEN
to be generated
CFG_DN
TBD
TBD
TBD
TBD
OPEN
to be generated
IRQ_DN
TBD
TBD
TBD
TBD
OPEN
to be generated
COVERAGE
TBD
TBD
TBD
TBD
OPEN
link_matrix.csv
Planning template only; confirm every value after complex-die and DWR insertion.
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]

## Slide 21
BACKUP · PATTERN TRACE
21
Pattern sign-off requires a traceable access transaction.
TRANSACTION TIMELINE · CONCEPTUAL TRACE, NOT A CYCLE-EXACT PATTERN
CAPTURE
CE
Load current TDR / instrument response
SHIFT
SE
Serially move instruction, SIB, or data bits
UPDATE
UE
Commit the shifted value to the update register
OBSERVE
IDLE / NEXT
Compare TDO or begin the next access transaction
SIGNAL-LEVEL TRACE CHECKLIST
SIGNAL / ITEM
TRACE QUESTION
EXPECTED INTERPRETATION
COMMON MISREAD
CE
Which capture register is active?
Loads a response before the corresponding shift.
Treating capture as data output itself.
SE
Which serial segment is selected?
Only the active scan segment shifts on the defined scan edge.
Assuming every SIB / TDR shifts together.
UE
Which update register commits?
Makes the shifted instruction or data take effect.
Expecting functional effect during shift.
SIB state
Open before the target shift?
Controls whether the downstream segment is in the scan path.
Reading SIB toggles as random activity.
TDI / TDO
What bit order and latency apply?
Input and response traverse the active concatenated path.
Comparing TDO with zero-cycle latency.
TDO_EN
Is pad enable or internal data being inspected?
Pad-level enable can differ from internal scan-data validity.
Using TDO_EN alone to infer internal TDO validity.
Clock edge
Which edge shifts and which edge is observed?
Checker sampling follows the generated procedure and model.
Comparing on the transition edge.
The checker should explain every phase transition and compare point; a visually plausible waveform is not sufficient.
DFT Integration Project · Internal Review
Notes: [Sources]
- Internal project content supplied by the presenter.
[/Sources]